## Slide 1
New York City’s East River
Roosevelt Island Tidal Energy (RITE) Project
Leading the Commercialization of Hydrokinetic Tidal Energy Systems
Ron Smith
New York Association for Energy Economics
March 22, 2012

## Slide 2: Marine & Hydrokinetic (MHK) Systems Roadmaps To Commercialization
Ocean Renewable Energy Coalition (OREC); US Marine and Hydrokinetic Renewable Energy Roadmap- October 2011.
MHK technologies represent the potential to provide up to ten percent of US
electricity consumption
REF: http://www.oceanrenewable.com/roadmap
The International Energy Agency's Ocean Energy Systems (OES) International Vision for Ocean Energy
The 3rd Phase SuperGen Marine Energy Research Consortium (UK)
Charting the Course: Canada’s Marine Renewable Energy Technology Roadmap; Ocean Renewable Energy Group (OREG); October 2011
The ORECCA Offshore Renewable Energy Roadmap (EU); and
The Chilean Energy Ministry and the British Embassy in Chile recently commissioned a marine energy strategy for Chile.

## Slide 3: MHK Power Potential
Worldwide Theoretical Potential – 270GW at 30% Capacity Factor
REF: International Energy Agency-Ocean Energy Systems (OES); website at
www.iea-oceans.org
Canada – Tidal-current – 6,300MW; River-current – 2,000MW
REF: Ocean Renewable Energy Group (Canadian MHK Trade Association)
http://www.oreg.ca
United States – 50.8GW – East Coast- 2,400MW; West Coast, Alaska, Hawaii – 48.4GW
REF: Assessment of Energy Production Potential from Tidal Streams in the United States,
US Department of Energy, 2011

## Slide 4: Tidal/Ocean Energy Devices
Most (> 40-50m depths)
  Marine Current Turbines
  Open Hydro
  Clean Current / Alstom
  Atlantis Resources
Verdant Power (< 40-50m depths)
  Greater application - sited near power needs
  Closer to shore or onshore - lower O&M, less transmission costs, if any
  Uniquely & easily scaled, fewer moving parts
  Higher efficiency & capacity factor
  Market leader - proven technology

## Slide 5: SEAI (Sustainable Energy Authority Ireland) “10 Years from Prototype to Commercialization”

## Slide 6: EPRI (Electric Power Research Institute) “10 Years from Prototype to Commercialization”
Experience - Variety of Technologies
Built & Field-tested
Three Different Prototypes
  Dual-ducted Horizontal Axis
  Ontario Power Generation
  Vertical Axis (Triple Helical)
Massachusetts State
  Unducted Horizontal Axis
  New York Power Authority (NYPA)
Installed & Operated 17 Turbines
Commercial Standard System
  Fifth Generation (Gen5) System
  Work Validated by U.S. DOE
  Design Initiated by NYU & NYPA

## Slide 7: New York City & the East River Roosevelt Island Tidal Energy (RITE) Project
Partners & Customers

## Slide 8: New York Power Authority & New York University Prototype Design & Bench Tests (1981-85)
Theory
Practical Economics
Blade Design
Rotor Dynamometry (U.S. Navy Lab)
NYU Prototype Turbine
  4.5-m Diameter Rotor
  Pakistan’s Bong Canal

## Slide 9: RITE Demo Project Six Mounted Bottom Units
12/2006 to 8/2009
Pre-commercial Units (Gen4)
  Power to Two Customers
    Gristedes
    R.I. Motorgate
Generator Units (5)
  60+ MWh Energy Produced
  7,000+ Operational Hours
  Excellent Water-Wire Efficiency (~35%)
  High Capacity Factor (~30%)
Dynamometer Unit (1)
7
Notes: My Apt: ~30 kWh per month. 1 kWh per day
Turbine: ~250 kWh per day (TIDAL)
60 MWh = 60,000 kWh = 2000 JC Apartment months = 165 JC Apartment years

## Slide 10: RITE Project - Phase 2 NYC’s East River, Grid-connected Array

## Slide 11: RITE Demo Project Deployment
5

## Slide 12: RITE Project - Phase 2 Control Room

## Slide 13: RITE Project - Phase 2 Power Generation

## Slide 14: RITE Project - Phase 2 “Six-Pack” Array Flow

## Slide 15: RITE Project - Phase 2 Results & Accomplishments
A Multi-turbine Array Installed, Reinstalled & Operated
Grid-connected, Power to End-users
Fully Bidirectional Tidal Operation
Fully Continuous, Automatic, Unattended Generation
Operation More than 9,000 Turbine-hours
Water-to-wire Efficiencies: 33 - 41%
Generated Power 77% of the Time
Capacity Factor  30%
Generated over 80 MWh into NYC grid

## Slide 16: RITE Project - Phase 2 Lessons Learned & Applied
      Experience Gained in All Aspects of KHPS Installation & Operation
      Environmental Studies – Proportional to Fish Density & Possible Effects
      Rotor Structural Failures – Addressed in Fifth Generation (Gen5) Rotor Redesign
      Need More Extensive Advance Velocity Measurements & Turbulence Intensity
      Array Spacing & Siting Informed by Hydrodynamic & Generation Data

## Slide 17: Fifth Generation (Gen5) Rotor Redesign KHPS Blade Tested to 7 m/s & Beyond

## Slide 18: Verdant Power Today
Verdant Power Today
Gen5 5m Kinetic Hydropower System (KHPS)
  5m KHPS In manufacture; blades; gearboxes; QMS
  Composite blade testing at NREL
  Significant improvements from Gen4 design
Roosevelt Island Tidal Energy (RITE) Project
  Commercial license Jan 2012; 1MW (30 turbines)
  2012-2013 Gen5 testing and initial operation
  Environmental monitoring ( RMEE)
Gen5 10m class KHPS
  Scale-up from 56kW to 470kW
  Design and prototype testing cycle underway
Project Development
  Tidal Sites: Canada; UK; Asia
  River Sites: Canada; CORE (demonstration)

## Slide 19: Roosevelt Island Tidal Energy (RITE) Project
www.theriteproject.com
FERC Pilot License Issued
FERC P-12611
Jan 23, 2012
Notes: This is a picture of the site from above the lower end of Manhattan.
You can see the U.N. in the bottom of the screen …
… and a tug and barge about to enter the Western channel from the South.
our power field will be in the Eastern channel, beginning just north of the Queensboro Bridge.

## Slide 20: FERC Pilot License Eligibility
(1) small; RITE project is 1.05 MW
(2) short term; License term is 10 years
(3) located in an environmentally non-sensitive area; RITE EA conducted shows likely no effects– but includes a $2.3M monitoring plan
(4) removable and able to be shut down on short notice; RITE will follow “adaptive management” if effects are observed
(5) removed, with the site restored, before the end of the license term unless the licensee obtains a new license; Opportunity for extension beyond 10-years and
(6) initiated by a draft application with appropriate environmental analysis; RITE analysis process was 2006-2012; 6 years.

## Slide 21: RITE Project - Phase 3 (2012-14) 1 MW = 10, Gen5, 5-m Class Triframes
“Six-Pack” Demo: 6 Turbines ~ 1.6 Acres
Commercial Project: 30, 5-m/35kW Turbines (10 Triframes) ~ 18 Acres
U.S. Federal Energy Regulatory Commission (FERC)
Recommends Pilot Commercial License to be Issued 2011

## Slide 22: RITE Pilot Project 30 Turbine Array – Flow Scales
MACRO SCALE
Around the greater array region
MESO SCALE
Through/around the turbine array
MICRO SCALE
Around one turbine
11

## Slide 23: RITE Project 3 Keys to Success
Ongoing Reliability and Longevity
  Generate Clean Renewable Energy – Gen5 will be Better
  High Water-Wire Efficiency and Capacity Factor
  Lessons Learned at RITE – Applicable to Commercial Build-Out
Improving Cost Effectiveness
  Advanced Computational Tools – Partnerships
  Gen5 Improvements – Less Parts & Sealing Improved
  Mounting – Move from Monopile to Tri-frame
Monitoring Environmental Compatibility
  RITE Demo Project Invaluable for Understanding Technology Interactions
  Improving on Understanding Fishery Interactions
  Specific Build-Out Monitoring Proposed
20

## Slide 24: RITE Project Economics
COST
TIME
19
Verdant Power

## Slide 25: Gen5, Commercial Standard System Tailored for Site, Using Triframes or Single Mounts
Deeper Water = Larger Rotor Diameter (m)
Faster Water (m/s) = Larger Generator (kW)
Rotor Size & Current Speed
Rotor | 2 m/s | 3m/s | 4m/s
5-m Class (5 to 7-m) | 28 kW | 95 | 224
7-m | 55 | 190 | 450
10-m Class (9 to 11-m) | 115 | 385 | 920
11-m | 138 | 470 | 1,110 kW

## Slide 26: Generic MHK Project Project Capital Costs / Expenditures (CapEx)
One (1) row of ten (10), Gen5, 10-m Class Triframes = 15 MW
  30 turbines – estimated CapEx: USD 2.4M per MW
Three (3) rows of ten (10), Gen5, 10-m Class Triframes = 50 MW
  90 turbines – estimated CapEx: USD 2.2M per MW
Five (5) rows of ten (10), Gen5, 10-m Class Triframes = 75 MW
  150 turbines – estimated CapEx: USD 2M per MW
Seven (7) rows of ten (10), Gen5, 10-m Class Triframes = 100 MW
  210 turbines – estimated CapEx: USD 1.8M per MW
Ten (10) rows of ten (10), Gen5, 10-m Class Triframes = 150 MW
  300 turbines – estimated CapEx: USD 1.5M per MW

## Slide 27: Moving forward - Opportunities
Desire for renewables
  Generation
  MHK industry = jobs
Significant resource
  Distributed generation
  Small and large pilot arrays
Kinetic Hydropower System works!
  High W-T-W efficiency
  Predictable; simplistic
  Environmentally compatible
Synergies with other renewables
  Co-location
  Cable/Trans/O&M efficiencies

## Slide 28: Contact Information
Ron Smith
Verdant Power, Inc
The Octagon
888 Main Street
New York, NY 10044
rsmith@verdantpower.com
www.verdantpower.com
www.theriteproject.com
USA: 212-888-8887 x601
The Octagon